## Slide 1: Arduino Workshop #6
The I2C bus
Notes: 24 – Arduino Uno
24 – USB Cable
24 – Red LED
72 – Yellow LED
96 – Green LED
192 – 220 Ω resistor
48 – 4.7 kΩ resistor
24 – SN74HC595N shift register DIP IC
24 – TC74A0-5.0V AT I2C Temperature sensor
24 – Jumper Wire sets
24 – Breadboards

## Slide 2: PowerPoint and Code
Github.com/EELabMan
Go To Repositories and find Arduino 6 I2C bus

## Slide 3: Standardizing Integrated Circuits
We will look at the common I2C protocol
  Pronounced “eye squared see” or “eye two see”
  Invented in the 1980’s by Philips
    Allowed relatively low speed communications for various IC’s\
    Standardized in the 90’s
    Other companies adopted and released compatible chips
    Generally known as “two wire”
      Because two wires lines are used for communications\
        A data and a clock
    I2C is a trademarked name
      Think Kleenex vs Tissues
      If an electronic item says “two wire compatible” it will be fairly certain to be I2C compatible

## Slide 4: I2C Hardware Design
I2C is unique in that it can handle multiple devices
  All share the same communication lines
    A clock signal (SCL)
    Bidirectional data line
      Used to send data back and forth between the master and slave (SDA)
      Notice that the I2C bus requires pull-up resistors on both data lines

## Slide 5: Hardware and pull up resistors
The value of the needed pull up resistors
  Depends on the slave devices
    Number attached and individual needs
    Specified on Data sheet
  4.7 ㏀ is fairly standard (and what we will be using)

## Slide 6: Communication Scheme and ID numbers
I2C can have multiple devices to share communication lines with a single “master” device
  The Arduino will act as the master device
    Responsible for initiating all communications
      Slave devices can not initiate communication only respond to requests from the master
        If not -- the communication line would be overwhelmed and data would drop

## Slide 7: Naming and communication
Each slave device has a unique 7-bit address (ID)
  Some I2C devices have selectable addresses
  Some I2C devices have a fixed address (from the factory)
    Temperature sensors are commonly preprogrammed with various IDs (to facilitate more than 1 sensor on a single bus)
When communication is initiate
  An ID is transmitted
    The slave device reacts to data on the bus only when it’s directed at their ID

## Slide 8: TC74 temperature sensor

## Slide 9: Things to notice from the Data sheet
Notice from this manufacture
  You can purchase eight different ID numbers
    You could put 8 of them on 1 I2C chip and read them independently
    As you are writing the program to interface w/ your temp sensor later… be aware of its ID

## Slide 10: Address selectable I2C
Some chips (AD7414 and AD 7415) have address select (AS) pins
  Allows you to configure the address of the device
  Below we see AD7414 has an “AS” pin with 3 possible ID numbers
    Depending on whether “AS” pin is left disconnected, is tied to VCC, or grounded

## Slide 11: Communicating with I2C temp probe
Steps vary for different chips (with different requirements for different devices)
Thankfully Arduino I2C library can be used to abstract away most of the difficult timing work
Basic steps though are:
Master sends a start bit
Master sends 7-bit slave address of device it wants to talk to
Master sends read (1) or write (0) bit
  Depending on the desired action
Slave responds with an “acknowledge” or ACK bit (a logic low)
Data is handled
  In write mode
    Master sends 1 byte of info at a time
    Slave responds ACK
  In Read mode
    Master receives 1 byte of info at a time
    Responds to slave with ACK

## Slide 12: Wire it up

## Slide 13: Things to note
You can use the serial to print out temps
  Its a digital signal
    no conversion needed to see the data as a degrees reading
  SDA and SCL are wired to pins a4 and a5
    They carry data and clock signal
    Recall A4 and A5 are multiplexed pins
      Between ADC and hardware I2C
      When you initialize the wire library
        Those pins connect to the ATMega’s I2C controller
          Enabling with the Wire object to I2C device via those pins
        This means you can't use these pins as analog inputs and use the wire directory
          They are reserved for communication with I2C devices

## Slide 14: Before you can code an I2C device
You need to know the communication scheme
  You need to know how to read the datasheet to determine this
  Using what you already know about how I2C works

## Slide 15: The takeaway from those two tables
You can both read and write to this I2C
  As shown in the first table
The TC74 has 2 registers
  Current temp (in 0C)
  Contains configurable info about the chip (inc. standby state and data ready state)
In order to read the temp we can look at table 4-3 and 4-4

## Slide 16: The setup of our code
The read byte section earlier outlines the process we should follow to read the temperature
Send to the device’s address in write mode and write “0” to indicate you want to read from the register
Send to the device’s address in read mode and request 8 bits (1 bite) of information from the device
Wait to receive all 8 bits
When in doubt about how to properly code a device - google is your friend (search for code examples that show what you need)

## Slide 17: The Code
Download read_temp.ino from GitHub.
Wire.beginTransmission()
  starts communication w/ a slave with the given ID
Wire.write()
  sends 0 indicating you want to read from the temperature registry
Wire.endTransmission()
  sends the stop bit
wire.requestFrom()
  prepares the master to receive 1 byte of data from the slave
Wire.available() [within the while loop]
  blocks the program from executing the rest of the code until data is available on the I2C line
Wire.read()
  The 8 bit value is read as an integer
The last section converts the temp into freedom units

## Slide 18: What you should see

## Slide 19: Temp monitoring system

## Slide 20: Wire the arduino

## Slide 21: Minor modification of previous program
The print statements should read
Serial.print(c);
Serial.print(“C,”);
Serial.print(f);
Serial.print(“F.”);
This allows you to easily parse the temps by the delimiting character (“,” and “.” respectively)
Next we need to add a shift register code (from last session)and mao the LEDs to the appropriate levels (the code given chose 240C to 310C but you can choose any level that works best for the room)

## Slide 22: The Code
Part 1
Part 2
Download temp_unit.ino from GitHub

## Slide 23: You should see
The LEDs light up and if you squeeze the temp sensor with your fingers making the temp go up, the LED’s should respond

## Slide 24: Writing a Process sketch
Download from GitHub
Things to change
The com port needs to match the computer
Pick a font you enjoy
Pick a font size that you want
Arduino Serial Monitor must be closed

## Slide 25: Stay tuned
Arduino 7 will cover the SPI bus.
We’ll wire two Digital Potentiometers!