## Slide 1: Arduino Workshop #6
The I2C bus
Notes: 24 – Arduino Uno
24 – USB Cable
24 – Red LED
72 – Yellow LED
96 – Green LED
192 – 220 Ω resistor
48 – 4.7 kΩ resistor
24 – SN74HC595N shift register DIP IC
24 – TC74A0-5.0V AT I2C Temperature sensor
24 – Jumper Wire sets
24 – Breadboards

## Slide 2: PowerPoint and Code
Github.com/EELabMan
Go To Repositories and find Arduino 6 I2C bus

## Slide 3: Standardizing Integrated Circuits
We will look at the common I2C protocol
  Pronounced “eye squared see” or “eye two see”
  Invented in the 1980’s by Philips
    Allowed relatively low speed communications for various IC’s
    Standardized in the 90’s
    Other companies adopted and released compatible chips
    Generally known as “two wire”
      Because two wires lines are used for communications
        Data and a clock
    I2C is a trademarked name
      Think Kleenex vs Tissues
      If an electronic item says “two wire compatible” it will be fairly certain to be I2C compatible

## Slide 4: I2C Hardware Design
I2C is unique in that it can handle multiple devices
  All share the same communication lines
    A clock signal (SCL)
    Bidirectional data line
      Used to send data back and forth between the master and slave (SDA)
      Notice that the I2C bus requires pull-up resistors on both data lines

## Slide 5: Hardware and pull up resistors
The value of the needed pull up resistors
  Depends on the slave devices
    Number attached and individual needs
    Specified on Data sheet
  4.7 ㏀ is fairly standard (and what we will be using)

## Slide 6: Communication Scheme and ID numbers
I2C can have multiple devices to share communication lines with a single “master” device
  The Arduino will act as the master device
    Responsible for initiating all communications
      Slave devices can not initiate communication only respond to requests from the master
        If not -- the communication line would be overwhelmed and data would drop

## Slide 7: Naming and communication
Each slave device has a unique 7-bit address (ID)
  Some I2C devices have selectable addresses
  Some I2C devices have a fixed address (from the factory)
    Temperature sensors are commonly preprogrammed with various IDs (to facilitate more than 1 sensor on a single bus)
When communication is initiated
  An ID is transmitted
    The slave device reacts to data on the bus only when it’s directed at their ID

## Slide 8: TC74 temperature sensor

## Slide 9: Things to notice from the Data sheet
Notice from this manufacture
  You can purchase eight different ID numbers
    You could put 8 of them on 1 I2C chip and read them independently
    As you are writing the program to interface w/ your temp sensor later… be aware of its ID

## Slide 10: Address selectable I2C devices
Some chips (AD7414 and AD 7415) have address select (AS) pins
  Allows you to configure the address of the device
  Below we see AD7414 has an “AS” pin with 3 possible ID numbers
    Depending on whether “AS” pin is left disconnected, is tied to VCC, or grounded
Board Mount Temperature Sensors SMBus / 12C 10-bit digital temp sensor I.C.

## Slide 11: Communicating with I2C temp probe

## Slide 12: Before you can code an I2C device
You need to know the communication scheme
  You need to know how to read the datasheet to determine this
  Using what you already know about how I2C works
Notes: Steps vary for different chips (with different requirements for different devices)
Thankfully Arduino I2C library can be used to abstract away most of the difficult timing work
Basic steps though are:
Master sends a start bit
Master sends 7-bit slave address of device it wants to talk to
Master sends read (1) or write (0) bit
  Depending on the desired action
Slave responds with an “acknowledge” or ACK bit (a logic low)
Data is handled
  In write mode
    Master sends 1 byte of info at a time
    Slave responds ACK
  In Read mode
    Master receives 1 byte of info at a time
    Responds to slave with ACK

## Slide 13: Wire it up

## Slide 14: Things to note
You can use the serial to print out temps
  It’s a digital signal
    no conversion needed to see the data as a degree Celsius reading
  SDA and SCL are wired to pins a4 and a5
    They carry data and clock signal
    Recall A4 and A5 are multiplexed pins
      Between ADC and hardware I2C
      When you initialize the wire library. Those pins connect to the ATMega’s I2C controller. Enabling with the Wire object to I2C device via those pins

## Slide 15: The takeaway from those two tables
You can both read and write to this I2C
  As shown in the first table
The TC74 has 2 registers
  Current temp (in 0C)
  Contains configurable info about the chip (inc. standby state and data ready state)
In order to read the temp we can look at table 4-3 and 4-4
Notes: 2’s compliment - We need to base the code as an 8 bit 2’s compliment integer to read the sensor correctly.

## Slide 16: Upload the read_temp.ino
#include <Wire.h>
int temp_address = 72; //1001000 written as decimal number
void setup()
{
//Start serial communication at 9600 baud
Serial.begin(9600);
//Create a Wire object
Wire.begin();
}

## Slide 17: read_temp.ino Main Loop
void loop()
{
//Send a request
//Start talking to the device at the specified address
Wire.beginTransmission(temp_address);
//Send a bit asking for register zero, the data register
Wire.write(0);
//Complete Transmission
Wire.endTransmission();
//Read the temperature from the device
//Request 1 Byte from the specified address
Wire.requestFrom(temp_address, 1);
//wait for response

## Slide 18: read_temp.ino Main Loop cont.
while(Wire.available() == 0);
// Get the temp and read it into a variable
int8_t c = Wire.read();
//Do some math to convert the Celsius to Fahrenheit
int8_t f = round(c*9.0/5.0 +32.0);
//Send the temperature in degrees C and F to the serial monitor
Serial.print(c);
Serial.print("C ");
Serial.print(f);
Serial.println("F");
delay(500);
}

## Slide 19: What you should see in the Serial Monitor
Notes: Get the circuit chiller to test the negative numbers.

## Slide 20: Temp monitoring system

## Slide 21: Wire the arduino

## Slide 22: Minor modification of previous program
The print statements should read
Serial.print(c);
Serial.print(“C,”);
Serial.print(f);
Serial.print(“F.”);
This allows you to easily parse the temps by the delimiting character (“,” and “.” respectively)
Next we need to add a shift register code (from last session)and mao the LEDs to the appropriate levels (the code given chose 240C to 310C but you can choose any level that works best for the room)

## Slide 23: Download temp_unit.ino from GitHub
Notes: Click to open file

## Slide 24: You should see
The LEDs light up and if you squeeze the temp sensor with your fingers making the temp go up, the LED’s should respond

## Slide 25: Writing a Process sketch
Download from GitHub
Things to change
The com port needs to match the computer
Pick a font you enjoy
Pick a font size that you want
Arduino Serial Monitor must be closed

## Slide 26: Stay tuned
Arduino 7 will cover the SPI bus.
We’ll wire two Digital Potentiometers!